## Slide 1: Verilog Simulation & Debugging Tools
數位電路實驗
TA: 吳柏辰
Author: Trumen

## Slide 2: Outline
Environment Setup
NC-Verilog
nLint
nWave
Verdi

## Slide 3: Environment Setup

## Slide 4: Login to the Linux Server
Many EDA tools are provided only for the Linux OS.
So we have to use software like PuTTY/PieTTY/MobaXterm on our local computer to login to the linux server and use the EDA tools on it.

## Slide 5: NTUEE Linux Servers
IC Design Lab (TA:邱茂菱) http://cad.ee.ntu.edu.tw/
Server list
IP | NAME | TYPE | CPU | CPU CLOCK | MEMORY | OS
140.112.20.59 | cad16 | IBM X3400 | Intel Xeon 64 | 2.4 GHz * 16 | 100 G | RHEL 5
140.112.20.60 | cad17 | IBM X3550 | Intel Xeon 64 | 2.4 GHz * 16 | 20 G | RHEL 5
… | … | … | … | … | … | …
140.112.20.85 | cad42 | IBM X3500 | Intel Xeon 64 | 2 GHz * 24 | 32 G | CentOS 5

## Slide 6: X Window System
X Window System (X11, X, and sometimes informally X-Windows) is a windowing system for bitmap displays, common on UNIX-like (ex: Linux) operating systems.
Microsoft Windows is not shipped with support for X, but many third-party implementations exist, as free and open source software such as Cygwin/X, and proprietary products such as Xming.

## Slide 7: Introduction to MobaXterm (1/2)
MobaXterm is free software that can be installed onto your local Windows or Mac computer which provides a graphical user interface and a command line shell for the server.
Official Website http://mobaxterm.mobatek.net/

## Slide 8: Introduction to MobaXterm (2/2)
MobaXterm provides useful features for developers:
  Multitab terminal with embedded Unix commands (ls, cd, ...).
  Embedded X11 server for easily exporting your Linux display.
  Passwords management for SSH, SFTP, etc (on demand password saving).
  …

## Slide 9: Session Settings
Click the Session button and specify which session you want. Usually this will be SSH. For that click SSH.
1
2

## Slide 10
1
2
3

## Slide 11
2
1 (double-click)

## Slide 12: Command Line Shell
We can also use the command line shell to login to the server.
  ssh bXXXXX@cad27.ee.ntu.edu.tw [-p YYYYY]
    bXXXXX: your usesr name
    YYYYY: port number
      here -p 22 is redundant because 22 is the default port number.

## Slide 13: Upload Files (1/2)
Uploading files fom your local PC to the server.
1
2
3. Choose which file(s) to upload

## Slide 14: Upload Files (2/2)
Moving and copying files by using the drag-and-drop.
1
2

## Slide 15: Download Files (1/2)
2
1
Downloading files from the server to local PC.
3. Select directory

## Slide 16: Download Files (2/2)
Moving and copying files by using the drag-and-drop.
1
2

## Slide 17: NC-Verilog

## Slide 18: Introduction to NC-Verilog
The Cadence® NC-Verilog® simulator is a Verilog digital logic simulator.
We can use NC-Verilog to
  Compiles the Verilog source files.
  Elaborates the design and generates a simulation snapshot.
  Simulates the snapshot.

## Slide 19: Before Using NC-Verilog
Source the environment settings of CAD tools.
If you try entering the command "ncverilog" but it turns out "command not found," it means there's something wrong with the "*.cshrc" file or the software license is out of date.
source ~cvsd/cvsd.cshrc
Notes: 有些server輸入"source ~cvsd/cvsd.cshrc"後會出現command not found
這很有可能是false alarm，先輸入ncverilog檢查是否能夠使用
如果可以使用的話就沒問題了

## Slide 20: Running Verilog (1/2)
Run the Verilog simulation:
Another choice of running Verilog simulation:
ncverilog testbench.v exp2.rsa.v +access+r
ncverilog -f exp2_rsa.f +access+r
In exp2_rsa.f

## Slide 21: Running Verilog (2/2)
"+access+r" is added to enable waveform file dumping.
*.fsdb has smaller file size than *.vcd. But $fsdbDumpfile cannot work without sourcing verdi.cshrc.
In testbench.v, line 69~72
or

## Slide 22: Simulation Results
Check the simulation result to see if the Verilog design is finished correctly.

## Slide 23: nLint

## Slide 24: Introduction to nLint
nLint is a comprehensive HDL design rule checker fully integrated with the Debussy debugging system (Developed by SpringSoft).
We can use nLint to check the coding style of our design and if it is synthesizable.

## Slide 25: Before Using nLint
Source the environment settings of CAD tools.
To avoid the warning *WARN* Failed to check out license. occurs when starting nLint, please type the following command:
source ~cvsd/verdi.cshrc
setenv LM_LICENSE_FILE '26585@lsntu:26585@lsncku'

## Slide 26: Start nLint
Type the following command:
  The token "&" enable you to use the terminal while nLint is running in the background.
nLint -gui &
Just ignore this warning.

## Slide 27: Specify the Design File
1

## Slide 28
1
2
3
4
5

## Slide 29: Start Checking
1

## Slide 30
Not all the warnings or errors are valuable.

## Slide 31: nWave

## Slide 32: Introduction to nWave
nWave is one of the best waveform (*.vcd or *.fsdb) viewer.
We can debug easily by checking the waveform file dumped during simulation.

## Slide 33: Before Using nWave
Source the environment settings of CAD tools.
To avoid the Verdi warning window occurs, please type the following command:
source ~cvsd/verdi.cshrc
setenv LM_LICENSE_FILE '26585@lsntu:26585@lsncku'

## Slide 34: Start nWave
Type the following command:
  Also, the token "&" enable you to use the terminal while Verdi is running in the background.
nWave &
Just ignore this warning.

## Slide 35: Open the FSDB File
1

## Slide 36
1
2
3

## Slide 37: Choose Signals
1

## Slide 38
Choose signals we are interested in.
1
2
3
4

## Slide 39: Browse the Whole Waveform
1

## Slide 40: Browse the Specified Interval
press & drag

## Slide 42: Search for Specified Signal
1
2
3
4,5,…

## Slide 43
cursor position
(Search by rising oe)
Jump to the cursor position (Used when we are lost)

## Slide 44: Change Sign Representation
1
2
3

## Slide 45: Change Radix Representation
2
1
3
4

## Slide 47: Change Signal Position
1
2
Press middle mouse button,
drag and then drop.

## Slide 49: Signal Aliasing
1
2
3
4

## Slide 50
1
2
3
Note that signal aliasing is a strict one-to-one correspondence so the value represented in the viewer must exactly represent what format your filter expects. (e.g., binary, hexadecimal)
4
5
6

## Slide 52: Reload the Waveform
Remember to reload the waveform whenever finishing another Verilog simulation.
1

## Slide 53: Verdi

## Slide 54: Introduction to Verdi
The Verdi Automated Debug System is an advanced open platform for debugging digital designs with powerful technology that helps you:
  Comprehend complex and unfamiliar design behavior.
  Automate difficult and tedious debug processes.
  Unify diverse and complicated design environments.

## Slide 55: Basic Function (1/2)
nTrace
  A source code viewer and analyzer that operates on the knowledge database (KDB) to display the design hierarchy and source code (Verilog, VHDL, SysmVerilog, SystemC, PSL, OVA, mixed) for selected design blocks.
  The main window of Verdi.

## Slide 56: Basic Function (2/2)
nWave
  A state-of-the-art graphical waveform viewer and analyzer that is fully integrated with Verdi's source code, schematic, and flow views.
nSchema
  A schematic viewer and analyzer that generates interactive debug-specific logic diagrams showing the structure of selected portions of a design.
These two tools can be opened through nTrace.

## Slide 57: Before Using Verdi
Source the environment settings of CAD tools.
To avoid the Verdi warning window occurs, please type the following command:
source ~cvsd/verdi.cshrc
setenv LM_LICENSE_FILE '26585@lsntu:26585@lsncku'

## Slide 58: Start Verdi
Type the following command:
  Also, the token "&" enable you to use the terminal while Verdi is running in the background.
verdi &
Just ignore this warning.

## Slide 59: nTrace
1

## Slide 60
1
2
3
4
5

## Slide 61
Hierarchical
Browser
Netlist Code
Window
Message
Window
1 (double-click)

## Slide 62
1
double-click
1
Notes: 同號表示兩者等意
like "Go to Declaration" in visual studio

## Slide 63
1
double-click
1
Notes: 同號表示兩者等意
like "Go to Definition" in visual studio

## Slide 64
1

## Slide 65
1

## Slide 66
2
1

## Slide 68
2
1

## Slide 70: nSchema
1

## Slide 71
1 (double-click)
Push View In

## Slide 72
1

## Slide 74
2
1 (right-click)

## Slide 75
2
1 (right-click)

## Slide 77: nWave
1

## Slide 78
1
1
2
3

## Slide 79
1
Press middle mouse button,
drag and then drop.

## Slide 81
1
Ctrl + C

## Slide 82
1 (right-click)
2

## Slide 84
2
1

## Slide 85
1

## Slide 86
1

## Slide 89: The End.
Any question?

## Slide 90: Reference
"MobaXterm User Manual“ by The Centre for eResearch, University of Auckand.
"Cadence NC-Verilog Simulator Tutorial“ by Cadence
"Quick Start: an nLint Tutorial" by NOVAS
"Introduction to Verdi" by Abel Hu
"Verdi3 datasheet" by Synopsys